## Slide 1: Introduction to Operating Systems CS/COE 1550
Spring 2020-2021
Sherif Khattab
ksm73@pitt.edu
(Some slides are from Silberschatz, Galvin and Gagne ©2013)

## Slide 2: Announcements
Upcoming deadlines:
  3/26: Lab 3, Quiz 2, and Homework 9
  4/2: Project 3 (Virtual Memory Simulator)
  Tophat questions due one week after each lecture

## Slide 3: Last Lecture …
Modeling of Page Replacement Algorithms
Address Translation
  Single-level Page Table

## Slide 4: Muddiest Points (1/2)
Even though I feel like I know how to calculate waiting/response times, every time I try to actually do it it seems like something always goes wrong
Still catching up on lectures.
Address Translation
  memory and paging structures
  relation between page size and table size and how the logical address size affects them
  still kind of confused on calculating page numbers
  Does the page table hold physical or virtual addresses? When are they translated?
  What does the page offset do when accessing the memory on the last step of the address translation architecture?
  page number vs offset
  Will the offset bits always be 32- the page bits?
  The second tophat question (I understand how you got the answer, but I don't understand why that was the correct process to get it). And converting page numbers when transforming from logical --> physical
  Logical address to page frame calculations
the point of a dirty bit
Belady's Algorithm

## Slide 5: Address Translation Structures

## Slide 6: Address Translation Relations

## Slide 7: Page number vs. Offset

## Slide 8: Muddiest Points (2/2)
HW 8
  question 1
  questions 6 and 7
Page Replacement Algorithms
  Why do some algorithms suffer from Belady's anomaly and how do stack algorithms avoid this issue?
  lru trace
    Could you run through the LRU diagram example and explain how it works( from slide 9)
  Stack Algorithms
    Getting the number of page faults from the stack algorithm
    distance in stack algorithm
    What does it takes for the stack algorithm to save all of those
    Why do we use distance in a 2D structure instead of a counter to keep track of page faults?
    what are some other stack algorithms?
    How are the distances in memory used to count the number of page faults in LRU?
    The logic behind adding extra rows for stack algorithms
    How can you predict the number of page faults again?
Project 3
  Getting it started
  Creating the programming version of the paper solution sounds pretty abstract, but I think once I do it for myself it will clear more things up

## Slide 9: HW 8 Q1

## Slide 10: HW 8 Q6

## Slide 11: Hash Table for OPT in Project 3

## Slide 12: Today’s Agenda …
Address Translation
  2-level Page Table
  TLB

## Slide 13: Two-level page tables
Problem: page tables can be too large
  232 bytes in 4KB pages need 1 million PTEs
Solution: use multi-level page tables
  “Page size” in first page table is large (megabytes)
  PTE marked invalid in first page table needs no 2nd level page table
1st level page table has pointers to 2nd level page tables
2nd level page table has actual physical page numbers in it
884
960
955
. . .
220
657
401
. . .
1st level page table
2nd level page tables
. . .
. . .
. . .
. . .
. . .
. . .
. . .
. . .
. . .
main memory
. . .
125
613
961
. . .

## Slide 14: More on two-level page tables
Tradeoffs between 1st and 2nd level page table sizes
  Total number of bits indexing 1st and 2nd level table is constant for a given page size and logical address length
  Tradeoff between number of bits indexing 1st and number indexing 2nd level tables
    More bits in 1st level: fine granularity at 2nd level
    Fewer bits in 1st level: maybe less wasted space?
All addresses in table are physical addresses
Protection bits kept in 2nd level table

## Slide 15: Two-level paging: example
System characteristics
  8 KB pages
  32-bit logical address divided into 13 bit page offset, 19 bit page number
Page number divided into:
  10 bit page number
  9 bit page offset
Logical address looks like this:
  p1 is an index into the 1st level page table
  p2 is an index into the 2nd level page table pointed to by p1
p1 = 10 bits
p2 = 9 bits
offset = 13 bits
page offset
page number

## Slide 16: 2-level address translation example
. . .
. . .
p1 = 10 bits
p2 = 9 bits
offset = 13 bits
page offset
page number
. . .
0
1
p1
. . .
0
1
p2
19
physical address
1st level page table
2nd level page table
main memory
0
1
frame number
13
Page table base
. . .
. . .

## Slide 17: Translation Lookaside Buffer (TLB)
Search the TLB for the desired logical page number
  Search entries in parallel
  Use standard cache techniques
If desired logical page number is found, get frame number from TLB
If desired logical page number isn’t found
  Get frame number from page table in memory
  Replace an entry in the TLB with the logical & physical page numbers from this reference
Logical page #
Physical frame #
Example TLB
8
unused
2
3
12
29
22
7
3
1
0
12
6
11
4

## Slide 18: Handling TLB misses
If PTE isn’t found in TLB, OS needs to do the lookup in the page table
Lookup can be done in hardware or software
Hardware TLB replacement
  CPU hardware does page table lookup
  Can be faster than software
  Less flexible than software, and more complex hardware
Software TLB replacement
  OS gets TLB exception
  Exception handler does page table lookup & places the result into the TLB
  Program continues after return from exception
  Larger TLB (lower miss rate) can make this feasible